## Slide 1
DIGITAL PIANO FINAL PROJECT
01
STM32 NUCLEO-L476RG Digital Piano
Four push buttons select notes. Two potentiometers control octave and volume. SysTick generates three speaker square waves.
Final behavior
Press one button and the board plays a simple three-note chord. PA5, PA6, and PA7 each use a separate counter, so AD2 can show three different frequencies at the same time.
Hardware used
PA5 -> speaker output 1
PA6 -> speaker output 2
PA7 -> speaker output 3
PC0-PC3 -> push buttons
PA0 -> volume potentiometer
PA1 -> octave potentiometer
Course focus: GPIO, EXTI, SysTick, ADC, bit masks, and modular C files.

## Slide 2
PROJECT GOALS
02
The project combines lecture modules into one working embedded system.
Each feature maps directly to a course topic, so the project can be explained from the registers up.
GPIO output
PA5, PA6, and PA7 are configured as push-pull outputs for the speaker signals.
GPIO input + EXTI
PC0 to PC3 use pull-ups and external interrupts for button press and release.
SysTick timing
A 20 kHz SysTick interrupt creates the square-wave sound signals.
ADC control
PA0 and PA1 are analog inputs for the volume and octave potentiometers.

## Slide 3
HARDWARE MAP
03
Every pin has one job, which keeps debugging simple.
The speaker outputs are on GPIOA. The buttons are on GPIOC. The potentiometers use ADC1 channels.
STM32L476RG
NUCLEO Board
PC0 Button 1
PC1 Button 2
PC2 Button 3
PC3 Button 4
PA5 Speaker 1 / root
PA6 Speaker 2 / third
PA7 Speaker 3 / fifth
PA0 Volume ADC PA1 Octave ADC

## Slide 4
SYSTEM ARCHITECTURE
04
System Architecture Block Diagram
Push Buttons
PC0/PC1/PC2/
PC3
Octave
Potentiometer
PA1 / ADC
Volume
Potentiometer
PA0 / ADC
NUCLEO-L476RG MCU
GPIO/EXTI
Button Inputs
Main Control
Logic Chord
Selection
SysTick
Sound Engine
20 kHz Timing
Speaker Outputs
PA5/PA6/PA7

## Slide 5
SOFTWARE FLOWCHART
05
Main loop sleeps most of the time; interrupts do the timing work.
This is the software flowchart to focus on during the presentation.
Power on
Initialize
GPIO, SysTick,
EXTI, ADC
while(1)
__WFI()
Read ADC
every 20 ms
Get active
button
No button?
Stop_Tone()
Play_Tone(freq)
SysTick_Handler
20 kHz
makes sound
Button press/release wakes CPU through EXTI. SysTick keeps running in the background for audio.

## Slide 6
SYSTICK SOUND ENGINE
06
Three independent counters create three speaker frequencies.
Each output has its own half-period, counter, phase, and volume high-time.
PA5
half_1 / count_1 / phase_1
root note
PA6
half_2 / count_2 / phase_2
third
PA7
half_3 / count_3 / phase_3
fifth
if(count_1 >= half_1){
count_1 = 0;
phase_1 ^= 1;
}
if(phase_1 == 1)
GPIOA->ODR |= PA5_MASK;
else
GPIOA->ODR &= ~PA5_MASK;
Direct GPIOA->ODR writes are used inside SysTick because the interrupt must stay short and fast.

## Slide 7
INPUTS AND CONTROLS
07
Buttons and potentiometers change the sound without stopping SysTick.
EXTI handles fast button changes. ADC is read every 20 ms so the knobs feel smooth.
Button path
PC0-PC3 use pull-up resistors.
Falling edge means button press.
Rising edge means button release.
50 ms debounce avoids false presses.
active_note stores the held button.
ADC path
PA0 reads the volume potentiometer.
PA1 reads the octave potentiometer.
ADC values are 0 to 4095.
8 samples are averaged.
Volume becomes 0 to 100 percent.
main.c combines both paths:
active button + octave + volume

## Slide 8
DEMO AND VALIDATION
08
The demo proves the software flow by checking sound, controls, and AD2 waveforms.
The strongest explanation is to connect each visible behavior back to one part of the code.
Live demo steps
1. Press each push button.
2. Release button and show sound stops.
3. Turn volume knob down and up.
4. Turn octave knob and show pitch change.
5. Show AD2 on PA5, PA6, and PA7.
Expected AD2 result
For button 1, the outputs should be close to:
PA5 about 262 Hz
PA6 about 330 Hz
PA7 about 392 Hz
Values shift when the octave knob changes.
Defense points
No HAL: register-level setup.
EXTI detects button edges.
ADC reads both potentiometers.
SysTick creates audio timing.
Direct ODR writes keep ISR fast.
Closing sentence: This project combines GPIO, EXTI, ADC, SysTick, and modular C into one working embedded piano.